## Slide 1
MARCH: MAze Routing
Under a Concurrent and Hierarchical Scheme
for Buses
Speaker:
Jingsong Chen
Authors:
Jingsong Chen, Ph.D. student, CSE, CUHK
Jinwei Liu, Ph.D. student, CSE, CUHK
Gengjie Chen, Ph.D. student, CSE, CUHK
Dan Zheng, Ph.D. student, CSE, CUHK
Evangeline F. Y. Young, Professor, CSE, CUHK

## Slide 2
Problem Formulation
Our Methodology: MARCH
Experimental Results
Conclusion
Outline

## Slide 3: Outline
Problem Formulation
Our Methodology: MARCH
Experimental Results
Conclusion

## Slide 4
*This case comes from the slides “ICCAD 2018 CAD Contest Problem B Summary” (link: http://iccad-contest.org/2018/)
L2
L1
A toy case*
Problem Formulation
Input:
  A set of routing layers
    With preferred track direction for each layer
    With min spacing constraint for each layer
    With design boundary for each layer
    With a set of obstacles for each layer
  A set of routing tracks
    With wire width constraint for each track
  A set of buses
    With a set of bits to be routed on tracks for each bus
    With width constraint for each layer for each bus
    With pin shapes for each bit in a bus
Pin 0
Pin 1
Track
Obstacles

## Slide 5
Problem Formulation
*This case comes from the slides “ICCAD 2018 CAD Contest Problem B Summary” (link: http://iccad-contest.org/2018/)
A toy case*
L2
L1
Output:
  A set of on-track wires and vias that connect pins for all buses
    The bits in the same bus must share the exactly same topology
Pin 0
Pin 1
Via
Wire

## Slide 6
Problem Formulation
Wire length
Segment number
Compactness
Better
Worse
Routing cases*
*These cases come from the slides “ICCAD 2018 CAD Contest Problem B Summary” (link: http://iccad-contest.org/2018/)
Evaluation rule:
  Overall cost consists of routing cost and penalty cost
    Routing cost is the summation of :
      Wire length cost: shorter -> better
      Segment cost: less -> better
      Compactness cost: more compact -> better

## Slide 7
Problem Formulation
Spacing constraint*
*This figure comes from the slides “ICCAD 2018 CAD Contest Problem B Summary” (link: http://iccad-contest.org/2018/)
Evaluation rule:
  Overall cost consists of routing cost and penalty cost
    Penalty cost is the summation of:
      Spacing violation penalty
      Routing failure penalty
        Wire off-track
        Track width violation
        Bit open
        Topology inconsistency
p1
p2
L1
S1
S1
S1
S1
O1
Four types of topology inconsistency
2
1
2
1
1
1
2
2
M1
M2
M3
2
1
2
1
2
1
3
1
2
3

## Slide 8
Problem Formulation
Our Methodology: MARCH
Experimental Results
Conclusion
Outline

## Slide 9
Our Methodology: MARCH
If routing bit by bit:
  Advantage: traditional routing methods can be applied naturally.
  Disadvantage: topology consistency can hardly be maintained in a relatively complex routing environment.
Pin
Obstacle
M1 Track
M2 Track
Wire

## Slide 10
Our Methodology: MARCH
Two key features of MARCH:
  Hierarchically: a topology-aware path planning (coarse-grained) and a track assignment for bits (fine-grained).
  EFFICIENCY
  Concurrently: route all the bits in a bus concurrently.
  CORRECT-BY-CONSTRUCTION

## Slide 11
Our Methodology: MARCH
Data Structures:
  Bus-based Grid Graph (BGG):
    A multilayer grid graph with uniform grid cells (G-cells)
    A row of G-cells, named frontline, is the propagation unit in routing process.
    Each edge stores edge capacity for the bus and history cost.
  Track occupancy of each track:
    Record the positions of the track segments which cannot be used since:
      Occupied by obstacles
      Occupied by the routed wires of the other buses
Track
Occupied by Obstacle
Edge
Obstacle
Routed Wire
Occupied by Routed Wire
e1
e2
e3
e5
e4
e6
spacing constraint
t1
t2
t3
t4
t5
frontline
Track occupancy of t1

## Slide 12
Our Methodology: MARCH
The overall flow of MARCH:
  Initialization
    Construct a BGG with empty edge capacities
  Inner loop for each bus b:
    Update the BGG for b:
      Edge capacities meeting width constraint
      Pin locations
    Generate a routing path consisting of a set of rectangular regions in topology-aware path planning (TAP)
    Assign the track segments to the bits within each rectangular region in track assignment for bits (TAB)
    Update the track occupancies of all the tracks by the routed b
  Outer loop for rip-up and reroute (RR):
    Add history cost to the edge of BGG
    Enlarge the frontline size
Initialization
Bus-based Grid Graph (BGG) Update
Topology-aware Path Planning (TAP)
Evaluation & Best Solution Update
Need Rip-up and Reroute (RR)?
Final Solution
Y
N
Obstacle Info
Track Info
Bus
Info
Track Assignment for Bits (TAB)
Track Occupancy Update
All Buses Routed?
Y
N

## Slide 13
Our Methodology: MARCH
Topology-aware Path Planning (TAP):
  Same layer propagation
  Layer switching
  Build routing paths for multi-pin buses
Pin 0
frontline F1
Pin 1
Pin 2

## Slide 14
Our Methodology: MARCH
Topology-aware Path Planning (TAP):
  Same layer propagation:
    Propagate the frontline along the track direction (F1 -> F2)
    Generate a TAP region (T1)
    Maintain running capacity which will only decrease when some tracks are broken midway
Pin 0
frontline F1
frontline F2
Pin 1
TAP region T1
F1
T1
F2
running capacity
F1 -> F2
(3, 2) -> (2, 1)
Pin 2

## Slide 15
Our Methodology: MARCH
Topology-aware Path Planning (TAP):
  Layer switching:
    Go from one layer to its upper layer or lower layer (F2 on L3 -> F3 on L2) through a switching node
Pin 0
frontline F2
Pin 1
L1
L2
L3
frontline F3
node N3
Pin 2

## Slide 16
Our Methodology: MARCH
Topology-aware Path Planning (TAP):
  Layer switching:
    Go from one layer to its upper layer or lower layer (F2 on L3 -> F3 on L2)
    Compute the max number of bits that can pass through the node
      Without any bottleneck edge: trivial
      With bottleneck edge(s):
        With bit order unchanged:
          Solved by a greedy method
        With bit order changed:
          Solved by the right recursive algorithm
          The efficiency can be guaranteed by pruning

## Slide 17
Our Methodology: MARCH
Topology-aware Path Planning (TAP):
  Build routing paths for multi-pin buses:
    Find the path between the source pin and one of the sink pins through the propagation from the source pin
    Start the propagation from the current path to connect to the next pin
    Repeat this process until all the pins are connected
Pin 0
Pin 2
TAP region T1
TAP region T2
TAP region T3
Pin 1
Pin 0
Pin 1

## Slide 18
Our Methodology: MARCH
Track Assignment for Bits (TAB)
  Track segment range estimation:
    By determining the column/row of G-cells where the bit will be routed
T2
Estimated Track Segment Range
Actual Routed Wires Segment
Occupied by Obstacle
Obstacle on M2
bit1
bit2
bit3
bit4
T3
T1
TAP Region on L1
TAP Region on L2

## Slide 19
Our Methodology: MARCH
Track Assignment for Bits (TAB)
  Track segment range estimation:
    By determining the column/row of G-cells where the bit will be routed
  Exact track selection:
    Three conditions:
      Satisfy the width constraint
      Have long enough track segment
      With as less as possible spacing violations
T2
Estimated Track Segment Range
Actual Routed Wires Segment
Occupied by Obstacle
Obstacle on M2
bit1
bit2
bit3
bit4
t1
t2
t3
t4
t5
t6
t7
T3
T1
TAP Region on L1
TAP Region on L2

## Slide 20
Our Methodology: MARCH
Track Assignment for Bits (TAB)
  Track segment range estimation:
    By determining the column/row of G-cells where the bit will be routed
  Exact track selection:
    Three conditions:
      Satisfy the width constraint
      Have long enough track segment
      With less spacing violations
  Exact track segment range assignment
    See the actual routed wires
T2
Estimated Track Segment Range
Actual Routed Wires Segment
Occupied by Obstacle
Obstacle on M2
bit1
bit2
bit3
bit4
t1
t2
t3
t4
t5
t6
t7
T3
T1
TAP Region on L1
TAP Region on L2

## Slide 21
Our Methodology: MARCH
Rip-up and Reroute Scheme (RR):
  Add history cost to the edge of BGG:
    To eliminate the congested regions on the BGG
    hnew = α · nvio + β · hold where nvio is the number of spacing violations on the edge, and α and β are weights.
  Enlarge the frontline size:
    To handle the insufficiency of violation-free routing resources
    Enlarge the frontline size of the bus by 1 on the layer where:
      The number of spacing violations in a TAP region is larger than the bit number in 2 successive RR iterations.

## Slide 22
Problem Formulation
Our Methodology: MARCH
Experimental Results
Conclusion
Outline

## Slide 23
Experimental Results
 | Characteristics |  |  |  | Metric Weights |  |  |  | 
 | bus no. | net no. | layer no. | track no. | wwire | wseg | wcom | wspace | wfail
beta1 | 34 | 1260 | 3 | 49209 | 5 | 1 | 5 | 8 | 2000
beta2 | 26 | 1262 | 3 | 49209 | 5 | 1 | 5 | 8 | 2000
beta3 | 60 | 665 | 3 | 22732 | 12 | 1 | 4 | 8 | 2000
beta4 | 62 | 698 | 3 | 22732 | 12 | 1 | 4 | 8 | 2000
beta5 | 6 | 1964 | 4 | 54150 | 8 | 1 | 5 | 8 | 2000
final1 | 18 | 1032 | 3 | 81226 | 10 | 1 | 5 | 10 | 2000
final2 | 70 | 1285 | 3 | 14209 | 10 | 1 | 5 | 10 | 2000
final3 | 47 | 852 | 4 | 21379 | 10 | 1 | 5 | 10 | 2000

## Slide 24
Experimental Results
 | First Place |  |  |  |  | Second Place |  |  |  |  | Third Place |  |  |  |  | MARCH |  |  |  | 
 | Croute | Cspace | Cfail | Ctotal | Time (s) | Croute | Cspace | Cfail | Ctotal | Time (s) | Croute | Cspace | Cfail | Ctotal | Time (s) | Croute | Cspace | Cfail | Ctotal | Time (s)
beta1 | 689 | 280 | 0 | 969 | 3600 | 701 | 5096 | 0 | 5797 | - | 641 | 8744 | 4000 | 13385 | - | 765 | 0 | 0 | 765 | 50
beta2 | 515 | 760 | 0 | 1275 | 3600 | 563 | 4904 | 0 | 5467 | - | 484 | 9472 | 2000 | 11956 | - | 578 | 0 | 0 | 578 | 9
beta3 | 1936 | 0 | 0 | 1936 | 71 | 2024 | 0 | 0 | 2024 | - | 1999 | 1928 | 0 | 3927 | - | 1942 | 0 | 0 | 1942 | 72
beta4 | 2192 | 0 | 0 | 2192 | 64 | 2271 | 0 | 0 | 2271 | - | 2250 | 1048 | 0 | 3298 | - | 2165 | 0 | 0 | 2165 | 39
beta5 | 119 | 1848 | 0 | 1967 | 3600 | 95 | 616 | 2000 | 2711 | - | 98 | 1216 | 2000 | 3314 | - | 118 | 1848 | 0 | 1966 | 12
final1 | 327 | 830 | 2000 | 3157 | 3317 | 367 | 2750 | 2000 | 5117 | - | 252 | 0 | 10000 | 10252 | - | 356 | 840 | 0 | 1196 | 352
final2 | 1824 | 4500 | 8000 | 14324 | 3600 | 1890 | 2990 | 8000 | 12880 | - | 1976 | 6910 | 0 | 8886 | - | 2071 | 1480 | 0 | 3551 | 199
final3 | 2966 | 490 | 10000 | 13456 | 3600 | 2678 | 300 | 2000 | 4978 | - | 4238 | 20 | 24000 | 28258 | - | 3313 | 150 | 0 | 3463 | 133
Avg. Ratio |  |  |  | 2.130 | 105.45 |  |  |  | 3.731 | - |  |  |  | 7.832 | - |  |  |  | 1.000 | 1.000
*The scores of top 3 teams of IC/CAD 2018 contest are provided by the contest organizer. A binary is also obtained from the first place to get its runtime information.

## Slide 25
Problem Formulation
Our Methodology: MARCH
Experimental Results
Conclusion
Outline

## Slide 26
Conclusion
We propose MARCH for bus routing:
  Have a hierarchical framework (TAP & TAB) for efficiency
  Route all the bits of a bus concurrently for topology consistency
  Apply a RR scheme to reduce the routing congestion
  Performance compared with the top contest teams
    Reduce spacing violations greatly
    Avoid any routing failure
    Have competitive routing costs
    Have a much shorter runtime

## Slide 27
Thank you for attention!

## Slide 28
Q & A